## Slide 1: BASC PROPOSAL REPORT
EN2053 – Robot Design and Competition
13.06.2020

## Slide 2: Overall Strategy
We have divided the task into six subtasks.
  Line following
  Wall following & pillar detection
  Circle navigation
  Box manipulation and color detection
  Ramp navigation
  Gate area navigation
We thought of handling each task in a modular manner
Switching between line following and wall following *
Ramp navigation will be done using a feedback loop of gyroscope and motors
Box manipulation is the most crucial subtask in the competition
  Two color sensors will be used
  A gripping mechanism for the box

## Slide 3: Power Plan
The robot will be powered by two Li-Po batteries
  7.4V 2200mAh 25C battery
  11.1V 2200mAh 25C battery
Three voltage regulators – all LM2596S
  9V supply for drive motors, Arduino MEGA and OLED display
  Two 5V supplies for sensors, servo motors and other components
Dual battery setup would allow easier voltage regulation with minimum losses and higher capacity so that we can run several rounds during testing
Battery level indicators will be used with both batteries to avoid over-drain of batteries
Two PCBs would be used to minimize the wiring
PCBs will be finalized after breadboard testing
DIP switches will be used to control each component during testing
Alternatives for 9V regulator: XH-M401 module or two XL6009 modules in parallel

## Slide 4: Task Delegation
Phase 1: Preliminary design
  Pamuditha: peripheral components, robot body, coordination
  Tharindu: box collection, color sensing
  Yasod: circle navigation, ramp navigation
  Vidura: gate area, arena
  Thieshanthan: wall following, pillar detection
  Yomali: line following, arena
Phase 2a: Virtual implementations
  Schematic and PCB: Thieshanthan, Vidura, Pamuditha,Tharindu
  Coding: Pamuditha, Tharindu, Yomali, Yasod
  Mechanical design: Yasod, Vidura, Yomali, Thieshanthan
Phase 2b: Actual implementation
Phase 3: Testing
Task delegation for phase 2b and phase 3 will be decided when the university starts.