## Slide 1: Algorithms
Line Following
Curved Wall Following
Ramp Climbing
Pillar detection
Gate Passing
Circle Navigation
Dotted Line following

## Slide 2: Line Following
PID will be used
Sensor panel with 8 TCRT5000 IR sensors
Outputs of sensor readings will be used to calculate the robot’s position on the line. Formula : here, si will be either 1(white) or 0(black). di will be values of each sensor.

## Slide 3: Curved Wall Following
Two VL530LX TOF sensors will be used on each side.
PID algorithm
Image about taking reading
Sensor reading output formula

## Slide 4: Circle Navigation
Detect the Circle
Navigate along the circumference until finding a radius
Look for box with front TOF, if found manipulate
Enter the circle by the radius
If the box found before reaching the center start manipulation
Otherwise, reach center and get readings from distance sensors
Locate the box
Manipulate

## Slide 5: Dotted Line Following(Need correction)
Detect end of a segment
Select the direction, and move a certain distance
Detect next segment
Adjust direction

## Slide 6: Ramp Climbing
Detect the ramp, using front TOF sensor or Gyro.
Increase Motor power
Adjust speed with response from Gyro sensors
Turn
Reduce speed while climbing down

## Slide 7: Pillar Detection
TOF sensors will be used to count the pillars
Adjust the course if needed
Proceed otherwise

## Slide 8: Gate Passing
Use front TOFs to identify closed gates
Distance to cover = x cm
7s time to cross, therefore required base speed y cm/s
Three possible scenarios
Gate 1 is Closed: Wait until it is opened, wait 3s, pass through both gates.
Gate 2 is closed(G1 open) : Wait until Gate 2 is opened, pass through both gates.
Both gates are open: Wait until a gate is closed, choose scenario 1 or 2.