## Slide 1: PROPOSAL REPORT
EN2532 – Robot Design and Competition
13.06.2020
BASC BATMAN'S ATTEMPT TO SAVE CATWOMAN

## Slide 2
Overall Strategy
We have divided the task into six subtasks.
Line following
Wall following & pillar detection
Circle navigation
We thought of handling each task in a modular manner
Switching between line following and wall following will be done by firing TOF sensors prior to the wall part *
Box manipulation is the most crucial subtask in the competition
  Two color sensors will be used
  A gripping mechanism for the box
Ramp navigation will be done using a feedback loop of gyroscope and motors
Box manipulation and color detection
Ramp navigation
Gate area navigation

## Slide 3
Sensors
The Raykha S8 IR sensor module
The TCS 3200 color sensor modules
2 sensors
one on the gripper to detect the front face
The other sensor to detect the bottom surface
VL530LX TOF sensor for distance measurement
2 sensors on either side for pillar and wall detection
1 sensor in front for the box detection
MPU 6050 Gyroscope

## Slide 4
The Processing Unit
Arduino MEGA2560
  Arduino modules have a wide range of libraries.
  The clock speed, flash memory, RAM and Interrupt count is higher than UNO/NANO
Raykha S8
Motor controller
Gyroscope
Arduino NANO
TOFs
Arduino MEGA
I2C bus

## Slide 5
The Processing Unit
Arduino NANO
  For Better modularity and debugging, use a separate controller for the box handling mechanism.
Servo motor control for gripper arm
Color sensor control
Calculation based on detected colors
Arduino NANO
A debugging interface, indicator LEDs are also connected to the main processor.

## Slide 6
Actuators – Gear motors
According to our calculations for the worst-case scenario in previous assignment (4)
  Total weight – 1.5 kg
  Torque require for a wheel – 0.777 kgcm
  Maximum stall torque - 1.036 kgcm
  Maximum power output – 0.144W
  Power require in climb down the ramp – 0.11W
  Maximum speed need in flat ground – 26.52 rpm
  For the above requirements we chose a motor which was Pololu 25D 12V high power 47:1 gear motor with encoders
  Main specifications
  No load speed & current – 210 rpm, 300 mA
  Stall torque & current – 12 kgcm, 5.6A@12V

## Slide 7
Actuators – Servo motors
According to our previous calculations on servo motors,
  Servo1 maximum torque = 0.115 kgcm
  Therefore we chose Tower pro SG90 servo for the servo1 & servo2.
    Main specifications
    Torque – 2.5 kgcm
    Operating voltage - +5V
  Servo3 maximum torque = 2.047 kgcm
Therefore we chose Tower pro SG5010 servo motor for servo3
Main specifications
Stall torque – 5.5 kgcm (4.8V)
Operating voltage – 4.8 – 6V

## Slide 8
Power Plan
The robot will be powered by two Li-Po batteries - dual battery setup
  7.4V 2200mAh 25C battery
  11.1V 2200mAh 25C battery
Three voltage regulators – all LM2596S
  9V supply for drive motors, Arduino MEGA and OLED display
  Two 5V supplies for sensors, servo motors and other components
Battery level indicators will be used with both batteries to avoid over-drain of batteries
Two PCBs would be used to minimize the wiring
PCBs will be finalized after breadboard testing
DIP switches will be used to control each component during testing
Alternatives for 9V regulator: XH-M401 module or two XL6009 modules in parallel

## Slide 9
Task Delegation
Phase 1: Preliminary design
  Pamuditha: peripheral components, robot body, coordination
  Tharindu: box collection, color sensing
  Yasod: circle navigation, ramp navigation
  Vidura: gate area, arena
  Thieshanthan: wall following, pillar detection
  Yomali: line following, arena

## Slide 10
Task Delegation
Phase 2a: Virtual implementations
  Schematic and PCB: Thieshanthan, Vidura, Pamuditha,Tharindu
  Coding: Pamuditha, Tharindu, Yomali, Yasod
  Mechanical design: Yasod, Vidura, Yomali, Thieshanthan
Phase 2b: Actual implementation
Phase 3: Testing
We are currently in the phase 2a.
Task delegation for phase 2b and phase 3 will be decided when the university starts.